## Slide 1: Cross-Track Infrared Sounder (CrIS) satellite observations of ammonia: Updates with initial application examples
Presenter: Mark Shephard
Environment and Climate Change Canada
Air Quality Research Division
EGU General Assembly
Vienna, Austria,
April 9th, 2019
Presentation: 18436

## Slide 2
Cross-track Infrared Sounder (CrIS) Satellite
  Physically based optimal estimation retrieval
  Retrieve NH3 profiles of volume mixing ratios (ppbv)
    Estimated errors and sensitivity (averaging kernels)
  Most sensitive to NH3 in boundary layer (< 3-km)
    Surface retrieved values are correlated with sensitivity in boundary layer
  Minimum detectability of ~0.5 ppbv (favourable conditions)
    Excellent instrument noise (~4x better than IASI)
      0.05K @270K for NH3 spectral region 967 cm-1
  NASA/NOAA CrIS instrument measures upwelling infrared radiation
  Twice a day temporal sampling: ~1:30 (afternoon and nighttime)
  14-km (diameter) spatial pixel size, global coverage
  2012-present : SNPP (fall 2011) & NOAA-20 (fall 2017) satellites
    Re-flights of sensor enables multi-decadal time series: e.g. 2038

## Slide 3: Example of CrIS NH3 profile retrievals in and around a forest fire plume in Northern Canada
Example of a scene containing low (background), moderate, and elevated (forest fire) NH3
Profile coloured to match surface plot
CrIS NH3 Profiles
CrIS Surface NH3 May 15, 2016
Profile Plot

## Slide 4: Daily spatiotemporal variability of surface NH3 over North America in August 2013
  Captures daily spatial distributions of ammonia
      For example: episodic events (e.g. forest fires)
      Impact of the meteorology, cannot “see” through thick clouds
True Colour: MODIS
Visible:
  Cloud (White)
  Smoke (blue/gray)
Infrared:
  Fire Detection (red)
CrIS
  Ammonia (NH3)
Notes: MODIS: Moderate Resolution Imaging Spectroradiometer

## Slide 5
  Captures expected spatiotemporal distributions of ammonia
Spatiotemporal variability of surface NH3 seasonally over North America (2013-2017 average)
Summer
Spring
Fall
Central Valley
US Mid-West
Lethbridge, AB
Wash. St.
Idaho
N. Carolina
Large Forest Fires (2014)
Spring fertilizer applications
Warmer temperatures
  More forest fires
  More volatilization
Spring fertilizer applications
Reduced concentrations over seasonal crop regions
  Cooler
  Less fertilizer application
  Less forest fires

## Slide 6
Annual Spatiotemporal Variability of Surface NH3 over North America (2013-2017)
  Captures spatial distributions of ammonia over expected “hot-spots” :
  Agriculture regions (e.g. Central Valley, US Mid-West, Lethbridge)
  Impact of large forest fires, especially in northern latitudes (e.g. 2014, 2015)

## Slide 7
Multi-year CrIS Surface NH3 Globally (2013-2017)
  Newly generated average global results
  Captures spatial distributions of ammonia over expected “hot-spots”

## Slide 8: Satellite Ammonia Evaluation
Remotely sensed satellite measurements require validation
Satellite provides global coverage, but at a lower spatial resolution than point source in-situ (e.g. ground- and aircraft-based) observations
  58 Ammonia Monitoring Network (AMoN) sites (USA) : bi-weekly
  10 National Air Pollution Surveillance Program (NAPS) sites (Canada) : 3-day
Preliminary assessment shows that the satellite and surface observations (AMoN) agree well despite sampling differences, especially for more homogenous conditions
Correlation of 0.76; Mean difference of +0.4 ppbv (~+15%)
Surface Site
Longwoods, Southern Ontario, Canada
Ground
Satellite
Notes: Surface Station Networks:
AMoN: Ammonia Monitoring Network (USA)
NAPS: National Air Pollution Surveillance Program (Canada)

## Slide 9: Satellite Ammonia Evaluation
Examples with similar seasonal patterns (correlated), but less agreement in magnitude
  Potential sampling differences in less homogeneous conditions
  Investigating making the satellite and ground-based comparisons more representative
Yosemite NP - Turtleback Dome, California (CA44) (elevation at ~1.5 km)
Central Valley Agriculture
Sierra Nevada Mountains
Detroit (MI96)
Yosemite NP - Turtleback Dome, California (CA44)
Detroit, Michigan (MI96)
Lake Erie
Ground
Satellite
Ground
Satellite
Notes: Surface Station Networks:
AMoN: Ammonia Monitoring Network (USA)
NAPS: National Air Pollution Surveillance Program (Canada)

## Slide 10: Satellite-derived dry deposition of reactive nitrogen (Nr) from NH3 and NO2 over North America
Dry deposition of NH3 resembles spatiotemporal patterns of concentrations
NH3 dry deposition flux peaks in agricultural and remote regions (e.g. Mid-West)
NO2 dry deposition flux dominates in urban regions (power plants) (e.g. North-East)
Flux = - Deposition Velocity x Surface Concentration
Modelled
Meteorological Data + Big-Leaf Model (BLM)
(Leiming Zhang et al., 2003 (ACP))
Satellite Observations
CrIS NH3 & OMI NO2
Shailesh Kharol
NH3 Dry Deposition Flux
Ratio, NO2 / (NH3 + NO2) Dry Deposition Flux
Mostly NH3
Mostly NO2
2013
Need validation data!
Notes: OMI: Ozone Monitoring Instrument (OMI): 2004 until present. Measures NO2 using UV/VIS part of the spectra.

## Slide 11: Satellite Derived Emissions: Fire Source
Emissions: mass / time
Rate mass leaves box
Winds from Weather Prediction Model
Mass in the box
Satellite Column Density x Area x MolecMass
Satellite (MODIS) image of smoke and hotspots from Canadian Fort McMurray fires
May 16 2016
EOSDIS Worldview
Combine satellite observations with model winds to derive fire emissions
Very large signal → single day emission estimates can be derived
cbc.ca
May 16 2016
Cristen Adams

## Slide 12: Satellite Derived Emissions: Fire Source
Satellite and model emissions agree pretty well for the Fort McMurray fires
Total Fort McMurray fire emissions are significant compared with anthropogenic
  This fire (burning for a month) is equal to ~20% of the annual anthropogenic emissions for the whole province of Alberta, Canada
Satellites
Models
Anthropogenic
Total Emissions
Fire Emission Models:
ECMWF Global Fire Assimilation System (GFAS)
Fireworks: ECCC Fireworks model
Emission Inventory:
ECCC Air Pollutant Emissions Inventory (APEI)

## Slide 13: Satellite Derived Emissions: Point Source (Ammonia Factories)
Weaker sources → use average of annual observations
Use wind rotation to orientate observations in upwind and downwind plume
Fit observations with Gaussian plume model to obtain emissions and lifetimes
TogliattiAzot, Russia
[CrIS, 2013-2018]
Donaldsonville ammonia, United States
[IASI-A, 2013-2018]
Satellites
Inventory
Satellites
Inventory
Examples where satellite derived emissions agree well with inventories for some locations, where others are completely missing in the current inventories
Enrico Dammers et al., in preparation
Notes: HTAPv2: Hemispheric Transport of Air Pollutants
NEI: National Emissions Inventory (US EPA)
E-PRTR: European Pollutant Release and Transfer Register

## Slide 14: Satellite Derived Emissions from Industry and Agriculture Sources
Emission estimates globally for larger industrial and agricultural sources (>6 kt/yr)
Generally the HTAPv2 global emissions inventory underestimates by a factor of 2
Average fitted NH3 lifetime for these sources is 2.5 ± 1 hr
Enrico Dammers et al., in preparation
CrIS – HTAPv2 Emissions
CrIS Emission Estimates
Agriculture dominated in HTAP
Industry
Emissions [kt/yr]
Difference [kt/yr]
Notes: HTAP: Hemispheric Transport of Air Pollutants
EDGAR: Emission Database for Global Atmospheric Research
GEM-MACH: Global Environmental Multi-scale Modelling air quality and Chemistry (GEM-MACH).

## Slide 15: Remarks
Provided examples of CrIS NH3 retrievals and initial applications
    Recently finished the global retrievals from 2013-2017 (v1.5)
      Still making improvements (average products)
      Good initial comparisons of satellite with ground-based observations
      Requires more validation: concentrations and dry deposition
Important applications we did not show here is the use of satellite observations for air quality model evaluation and data assimilation
Satellite remote sensing should be viewed as complimentary to conventional surface and aircraft monitoring
  Has advantages (i.e. fill in gaps in surface networks) and disadvantages (i.e. daily observations at regional scale (~10km))
Lots of progress → but still developing and exploring potential applications

## Slide 16: Contributions
Agriculture and Agri-Food Canada (AAFC), British Columbia, Canada
Atmospheric and Environmental Research (AER), Lexington, MA, USA
Environment and Climate Change Canada (ECCC), Toronto, Ontario, Canada
Environmental Monitoring and Science Division, Government of Alberta, Edmonton, Alberta, Canada (EMSD)
University of Toronto, Toronto, Ontario, Canada(UofT)
University of Waterloo, Waterloo, Ontario, Canada (UofW)
University of Bremen, Bremen, Germany IUP-Bremen
Universite Libre Bruxelles, Brussels, Belgium (ULB)
Satellite Ammonia | Karen Cady-Pereira (AER), Enrico Dammers (ECCC), Shailesh Kharol (ECCC;UofT), Jesse Thompson (ECCC,UofW), Andrew Kovachik (ECCC) , Yoni Gainariu-Matz (ECCC),Chris McLinden (ECCC), Chris Sioris (ECCC), Debora Griffin (ECCC), Martin Van Damme (ULB), Simon Whitburn (ULB), Lieven Clarisse(ULB) Pierre Coheur (ULB)
Validations | Enrico Dammers (ECCC), Shailesh Kharol (ECCC;UofT) Ed Hare (ECCC), Jason O’Brien (ECCC), Ewa Dabek (ECCC) AMoN and NAPS Data Providers
Model Evaluation | Shabtai Bittman (AAFC), Paul Makar (ECCC), Cynthia Whaley (ECCC), Junhua Zhang (ECCC) Leiming Zhang (ECCC)
Dry Deposition | Shailesh Kharol(ECCC;UofT); Leiming Zhang (ECCC)
Emissions | Enrico Dammers(ECCC), Vitali Fioletov(ECCC), Chris McLinden(ECCC)
+ others | 
THANKS!

## Slide 17: Background Slides

## Slide 18: Application to emissions
Emissions are derived by combining vertically-integrated profiles (columns) with winds from a meteorological reanalysis (here ECMWF)
We consider two approaches:
  Direct : Single overpass for larger sources  wild fires
  (similar to Mebust et al., ACP, 2011)
  Statistical : Multiple overpasses for smaller, more constant sources
   agricultural sources (Fioletov et al., GRL, 2015)
    requires the use of a rotation scheme in order to align the wind direction of all observations (Pommier et al., GRL, 2012; McLinden et al., Nature, 2016)

## Slide 19
1) Direct Method (simple)
  Applicable for larger sources where SNR is high and plumes can be resolved with a single overpass
  Satellite concentrations are directly combine with wind information to compute the flux density for a box around the emission source aligned with the wind, which is then integrated to get fire emission estimates
  Few sources meet this criteria
    e.g. Forest fires
Direct method for satellite emissions
= Concentration (molec/cm3)
= wind speed (cm/s)
= flux density (molec/cm2/s)
Estimated effective lifetimes are used to account for in-box loss
Wind

## Slide 20: Statistical Approach
2) Statistical method
  Resolution of satellite observations are large compare to the emissions
  Single-measurement has a lower SNR
NO2 over the oil sands from a single overpass of the Ozone Monitoring Instrument
To overcome these challenges we combine observations from many overpasses (weeks/months/year or more)
  This averaging leads to improved precision and effective spatial resolution
We use a rotation procedure which allows to combine observations from arbitrary wind direction
  Based on wind direction, individual satellite observations are reposition about a source such that all now share a common wind direction
Fit a plume model to the merged satellite + wind information to analyzed the downwind decay
  Providing estimates of emission rate (E) near the source and its average lifetime ().
  E = mass /  (steady-state assumption)

## Slide 21: Plume model and fitting (inversion)
Plume model assumes concentrations emitted from a point source decline exponentially in time and affected by turbulent diffusion that can be described by a 2D Gaussian function allowing for:
  1. Simple first-order loss (chemical transformations and deposition)
  2. Coarse spatial resolution (a smeared view by the satellite)
Stockie, SIAM Review, 2011
Downwind distribution
Cross-wind
distribution
convolution
Input Variables:
𝑥, 𝑦 distances of obs.
𝑢 wind speed [km/hr]
[molec/km2]
Fitted parameters:
emission rate
lifetime (decay time); (1/decay rate) [hr]
𝜎 plume width [km]; represents diffusion, and smoothing effect of the satellite
A non-linear fit of this plume function to the individual satellite observations (pixels) is used to derive estimates of 𝜎
Standard Gaussian Plume
exponential decay

## Slide 22
Satellite derived Dry Deposition Flux of NH3 & NO2
represents 24 h daily average flux
represents the satellite-derived ground-level concentration
represents hourly dry deposition velocity
is a concentration diurnal scaling factor.
For NO2:
represent hourly and satellite overpass time mean ground-level concentration from the GEM-MACH air quality model
We use the model diurnal profile to calculated the 24 hr daily average flux as follows:
For NH3:
Relatively limited information on the NH3 diurnal profile, and it can vary significantly by region and season. Thus, we presently assume that the mid-day satellite NH3 is representative of diurnal average (i.e., )
investigating this further using surface observations
Shailesh Kharol

## Slide 23: Any Fire Plume Heights Information?
Terra MODIS
True Color Composite 15th May 2016
Fort McMurray x
CALIPSO (70m) : LIDAR “pencil beam”
- High vertical resolution, but sparse coverage
Smoke Plume Heights of ~3km

## Slide 24: Satellite-derived reactive nitrogen (Nr) dry deposition from NH3 over North America (2013-2017)
Variability from year-to-year resembling the concentrations maps
Large forest fires impact on northern latitudes in some years (e.g. 2014)
Need more ground-based dry deposition measurements for validation!

## Slide 25: CrIS noise comparison with IASI and AIRS
Reference: Zavyalov, V., et al. (2013), Noise performance of the CrIS instrument, J. Geophys. Res. Atmos., 118,13,108–13,120, doi:10.1002/2013JD020457.
NH3 967 cm-1
CrIS ~0.05 K
AIRS ~0.15 K
IASI ~0.20 K